## Slide 1: BGP in 2013
Geoff Huston
APNIC
NANOG 60

## Slide 2
“The rapid and sustained growth of the Internet over the past
several decades has resulted in large state requirements for
IP routers. In recent years, these requirements are continuing
to worsen, due to increased deaggregation (advertising more specific
routes) arising from load balancing and security concerns..”
“Conventional “wisdom” about routing:
Quoted from a 2012 research paper on routing

## Slide 3
“The rapid and sustained growth of the Internet over the past
several decades has resulted in large state requirements for
IP routers. In recent years, these requirements are continuing
to worsen, due to increased deaggregation (advertising more specific
routes) arising from load balancing and security concerns..”
“Conventional “wisdom” about routing:
quote from a 2012 research paper on routing
Is this really true, or do we accept it as true without actually looking at the real behaviours of the Internet’s routing system???

## Slide 4
In this presentation we’ll explore the space of inter-domain routing (the Border Gateway Protocol – BGP
  We will look at the growth of the eBGP routing table over time and some projections for future growth
  Then we’ll look at the extent to which more specifics are dominating routing table growth ... or not

## Slide 5: The Big Picture of the v4 Routing Table

## Slide 6: The Big Picture of the v4 Routing Table
Introduction of
CIDR – March 1994
The Great Internet Boom
and Bust of 2000/2001
Broadband to the Masses
The GFC hits the Internet
Address Exhaustion

## Slide 7: The Routing Table in 2012-2013
Lets look at the recent past in a little more detail...

## Slide 8: IPv4 BGP Prefix Count 2011 - 2013
Jan
2011
Jan
2012
340,000
440,000
540,000
Jan
2013
Jan
2014

## Slide 9: IPv4 BGP Prefix Count 2013
Jan
2013
Apr
2013
430,000
460,000
490,000
Jul
2013
Oct
2013
25th June AS 7029 +3,606
AS 33363 +1,651
AS 4323 +1,351
AS 9116 + 348
Jan
2014

## Slide 10: IPv4 BGP Prefix Count 2013
Jan
2013
Apr
2013
430,000
460,000
490,000
Jul
2013
Oct
2013
Jan
2014

## Slide 11: As seen by peers of Route Views
AS131072

## Slide 12: IPv4 Routed Address Span: 2011 - 2013
130/8s
140/8s
150/8s
Jan
2011
Jan
2012
Jan
2013
Jan
2014

## Slide 13: IPv4 Address Pool

## Slide 14: IPv4 Address Pool

## Slide 15: That Unadvertised Address Pool
Appears to be relatively static in size since early 2011 at some 50 /8s, or 20% of the IPv4 global unicast space
At this stage its likely that ARIN and LACNIC will both hit their address pool exhaustion threshold levels at the end of 2014

## Slide 16: IPv4 Routed Address Span
156/8s
157/8s
158/8s
159/8s
Jan
2013
Apr
2013
Jul
2013
Oct
2013
Jan
2014
AS721 withdrew 33.0.0.0/8
AS80 withdrew 3.0.0.0/8
AS721 announced 33.0.0.0/8
AS721 withdrew 33.0.0.0/8

## Slide 17: IPv4 Routed AS Count
40,000
44,000
2010
2011
Jan
2011
Jan
2013
Jan
2012
Jan
2014
Jan
2015
36,000
48,000

## Slide 18: IPv4 2011 BGP Vital Statistics
Jan-13 Jan-14
Prefix Count 440,000 488,000 +11%
Roots 216,000 237,000 +10%
More Specifics 224,000 251,000 +12%
Address Span 156/8s 159/8s + 2%
AS Count 43,000 46,000 + 7%
Transit 6,100 6,600 + 8%
Stub 36,900 39,400 + 7%

## Slide 19: IPv4 in 2013 – Growth is Slowing
Overall Internet growth in terms of BGP is at a rate of some ~8-10% p.a.
  This is down by 33% from 2010
There was a single announcement event on 25 June of some 10K additional routes
Address span growing far more slowly than the table size

## Slide 20: IPv6 BGP Prefix Count
2,000
12,000
20,000
Jan
2011
Jan
2012
Jan
2013
Jan
2014
4,000

## Slide 21: IPv6 BGP Prefix Count
2,000
12,000
20,000
Jan
2011
Jan
2012
Jan
2013
Jan
2014
4,000
World IPv6 Day

## Slide 22: IPv6 Routed Address Span
Jan
2013
Jan
2012
Jan
2014
Jan
2015
0
30,000
60,000
90,000
Jan
2011

## Slide 23: IPv6 Routed AS Count
Jan
2011
Jan
2013
Jan
2012
Jan
2014
2,000
6,000
8,000
10,000
4,000
Jan
2015
World IPv6 Day

## Slide 24: IPv6 2011 BGP Vital Statistics
Jan-13 Jan-14 p.a. rate
Prefix Count 11,500 16,100 + 40%
Roots 8,451 11,301 + 34%
More Specifics 3,049 4,799 + 57%
Address Span (/32s) 65,127 72,245 + 11%
AS Count 6,560 7,845 + 20%
Transit 1,260 1,515 + 20%
Stub 5,300 6,330 + 19%

## Slide 25: IPv6 in 2013
Overall IPv6 Internet growth in terms of BGP is 20% - 40 % p.a.
  2011 growth rate was ~ 90%.
(Looking at the AS count, if these relative growth rates persist then the IPv6 network would span the same network domain as IPv4 in16 years time -- 2030!)

## Slide 26: BGP Size Projections
Generate a projection of the IPv4 routing table using a quadratic (O(2) polynomial) over the historic data
  For IPv4 this is a time of extreme uncertainty
    Registry IPv4 address run out
    Uncertainty over the impacts of any after-market in IPv4 on the routing table
  which makes this projection even more
  speculative than normal!

## Slide 27: IPv4 Table Size
2004
2010
0
600,000
2006
2012
2014
200,000
400,000
Linear: Y = -1692020 + (t * 1572.086)
Quadratic: Y = -2531405 + (2.824.189 * t) + (-4.667387* 10-13 * t2)
Exponential: Y = 10**(3.403664 + (year * 1.650395e-09))
2008
2016

## Slide 28: Daily Growth Rates
2006
2010
-800
0
800
2008
2012
2014
-400
400

## Slide 29: IPv4 Table Size
2004
2010
0
800,000
2006
2012
2014
200,000
400,000
2008
2018
600,000
1,000,000
2016

## Slide 30: IPv4 BGP Table Size predictions
Jan 2013 441,172 entries
2014 488,011 entries
2015 540,000 entries 559,000
2016 590,000 entries 630,000
2017 640,000 entries 710,000
2018 690,000 entries 801,000
2019 740,000 entries 902,000
* These numbers are dubious due to uncertainties introduced by IPv4 address exhaustion pressures.
Linear Model
Exponential Model

## Slide 31: IPv6 Table Size
2006
2010
0
20,000
30,000
2008
2012
2014
10,000
2016
40,000

## Slide 32: Daily Growth Rates
2006
2010
-40
0
40
2008
2012
2014
-20
20

## Slide 33: IPv6 Table Projection
2006
40,000
120,000
2009
2012
2018
2015
80,000
0

## Slide 34: IPv6 BGP Table Size predictions
Jan 2013 11,600 entries
2014 16,200 entries
2015 25,400 entries 19,000
2016 38,000 entries 23,000
2017 57,000 entries 27,000
2018 85,000 entries 30,000
2019 127,000 entries 35,000
* These numbers are dubious due to uncertainties introduced by IPv4 address exhaustion pressures.
Exponential Model
LinearModel

## Slide 35: Up and to the Right
Most Internet curves are “up and to the right”
But what makes this curve painful?
  The pain threshold is approximated by Moore’s Law

## Slide 36: Moore’s Law
As a rough rule of thumb, if the rate of growth of the table grows at a rate equal to, or less than Moore’s Law, then the unit cost of storing the forwarding table should remain constant
  Like all rough rules of thumb, there are many potential exceptions, and costs have many inputs as well as the raw cost of the the number of gates in a chip
  Despite this, Moore’s Law still a useful benchmark of a threshold of concern about routing growth

## Slide 38
Moore’s Law
BGP Table Size Predictions
IPv4 BGP Table size and Moore’s Law

## Slide 39: IPv6 Projections and Moore’s Law
Moore’s Law
BGP Table Size Predictions

## Slide 40: eBGP Table Growth
Nothing in these figures suggests that there is cause for urgent alarm -- at present
The overall eBGP growth rates for IPv4 are holding at a modest level, and the IPv6 table, although it is growing rapidly, is still relatively small in size in absolute terms
As long as we are prepared to live within the technical constraints of the current routing paradigm it will continue to be viable for some time yet

## Slide 41: BGP Updates
What about the level of updates in BGP?
Let’s look at the update load from a single eBGP feed in a DFZ context

## Slide 42: Announcements and Withdrawals

## Slide 43: Unstable Prefixes

## Slide 44: Convergence Performance

## Slide 45: IPv4 Average AS Path Length
Data from Route Views

## Slide 46: Updates in IPv4 BGP
Nothing in these figures is cause for any great level of concern …
  The number of unstable prefixes per day is growing at a slightly lower rate than the number of announced prefixes
  The number of updates per instability event has been constant, due to the damping effect of the MRAI interval, and the relatively constant AS Path length over this interval
What about IPv6?

## Slide 47: Announcements and Withdrawals

## Slide 48: Unstable Prefixes

## Slide 49: Convergence Performance

## Slide 50: IPv6 Average AS Path Length
Data from Route Views

## Slide 51: BGP Convergence
The long term average convergence time for the IPv4 BGP network is some 70 seconds, or 2.3 updates given a 30 second MRAI timer
The long term average convergence time for the IPv6 BGP network is some 90 seconds, or 3 updates

## Slide 52: BGP Table Growth
However ... continued scalability of the routing system relies on continued conservatism in routing practices.
How good are we at “being conservative” in routing?

## Slide 53: CIDR and BGP
To what extent do we still practice “conservative” routing and refrain from announcing more specifics into the routing table?
Are we getting better or worse at aggregation in routing?
What is the distribution of advertising more specifics? Are we seeing a significant increase in the number of more specific /24s in the routing table?

## Slide 54: An Example:
Prefix AS Path
193.124.0.0/15 4608 1221 4637 3356 20485 2118 ?
193.124.0.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.1.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.2.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.3.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.4.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.5.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.6.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.7.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.8.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.9.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.10.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.11.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.12.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.13.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.14.0/24 4608 1221 4637 3356 20485 2118 ?
193.124.15.0/24 4608 1221 4637 3356 20485 2118 ?
Origin AS: AS 2118 RELCOM-AS OOO "NPO Relcom"

## Slide 55: Who is doing this the most?
www.cidr-report.org

## Slide 56: More specifics in the Routing Table
Total Table Size
More Specifics

## Slide 57: More specifics in the Routing Table
Since 2002 more specifics account for ~50% of the
Routing Table. This has been a relatively constant
proportion over the past 12 years

## Slide 58: Does everyone see this?
% of entries that are more specific
-- as seen by peers of Route Views

## Slide 59: How much address space is announced by more specifics?
% of address space announced by more specifics –
-- as seen by peers of Route Views

## Slide 60: Does everyone announce more specifics?
332 Origin AS’s announce 50% of the total set of more specifics!

## Slide 61: Is it Everyone?
1% of the ASes (458 ASes) announce 54% of the more specifics (133,688 announcements)
55% of the ASes announce no more specifics
The top 20 ASes announce 40,404 more specifics

## Slide 62: The Top 20 of V4 More Specifics
AS Agg’s More Specifics
7029 148 4,275 WINDSTREAM - Windstream Communications Inc US
6389 50 2,979 BELLSOUTH-NET-BLK - BellSouth.net Inc. US
28573 685 2,727 NET Servicos de Comunicatio S.A. BR
17974 224 2,511 TELKOMNET-AS2-AP PT Telekomunikasi Indonesia ID
4323 449 2,486 TWTC - tw telecom holdings, inc. US
22773 159 2,167 ASN-CXA-ALL-CCI-22773-RDC - Cox Communications Inc. US
1785 121 2,030 AS-PAETEC-NET - PaeTec Communications, Inc. US
18566 19 2,029 MEGAPATH5-US - MegaPath Corporation US
7545 113 2,023 TPG-INTERNET-AP TPG Telecom Limited AU
36998 5 1,800 SDN-MOBITEL SD
18881 22 1,774 Global Village Telecom BR
8402 14 1,726 CORBINA-AS OJSC "Vimpelcom" RU
10620 1,035 1,661 Telmex Colombia S.A. CO
4755 179 1,632 TATACOMM-AS TATA Communications formerly VSNL is Leading ISP IN
4766 564 1,591 KIXS-AS-KR Korea Telecom KR
7552 26 1,232 VIETEL-AS-AP Viettel Corporation VN
9829 371 1,189 BSNL-NIB National Internet Backbone IN
7011 8 1,164 FRONTIER-AND-CITIZENS - Frontier Communications of America, Inc. US
9498 53 1,159 BBIL-AP BHARTI Airtel Ltd. IN
5617 36 1,150 TPNET Telekomunikacja Polska S.A. PL
20940 119 1,099 AKAMAI-ASN1 Akamai International B.V. US

## Slide 63: More specifics in the V6 Routing Table
Total Table Size
More Specifics

## Slide 64: More specifics in the V6 Routing Table

## Slide 65: Does everyone see this?
% of entries that are more specific
-- as seen by peers of Route Views

## Slide 66: How much V6 address space is announced by more specifics?
% of address space announced by more specifics –
-- as seen by peers of Route Views

## Slide 67: Are We Getting Any Better?
Take the daily top 10 ASes of advertisers of more specifics over the past 3 years and track the number of more specifics advertised by these ASes over the entire period

## Slide 68: Are We Getting any Better?
These AS’s were seen to be advertising the highest number of more specifics over the past 3 years:
1785 AS-PAETEC-NET - PaeTec Communications, Inc. US
2118 RELCOM-AS OOO "NPO Relcom" RU
3352 TELEFONICA-DATA-ESPANA TELEFONICA DE ESPANA ES
3356 LEVEL3 Level 3 Communications US
4323 TWTC - tw telecom holdings, inc. US
4538 ERX-CERNET-BKB China Education and Research Network Center CN
4755 TATACOMM-AS TATA Communications formerly VSNL is Leading ISP IN
4766 KIXS-AS-KR Korea Telecom KR
6389 BELLSOUTH-NET-BLK - BellSouth.net Inc. US
6503 Axtel, S.A.B. de C.V. MX
7011 FRONTIER-AND-CITIZENS - Frontier Communications of America, Inc. US
7029 WINDSTREAM - Windstream Communications Inc US
7545 TPG-INTERNET-AP TPG Telecom Limited AU
8402 CORBINA-AS OJSC "Vimpelcom" RU
10620 Telmex Colombia S.A. CO
11492 CABLEONE - CABLE ONE, INC. US
15557 LDCOMNET Societe Francaise du Radiotelephone S.A FR
17974 TELKOMNET-AS2-AP PT Telekomunikasi Indonesia ID
18566 MEGAPATH5-US - MegaPath Corporation US
22773 ASN-CXA-ALL-CCI-22773-RDC - Cox Communications Inc. US
28573 NET Servicos de Comunicatio S.A. BR
33363 BHN-TAMPA - BRIGHT HOUSE NETWORKS, LLC US
36998 SDN-MOBITEL SD

## Slide 69: Yes ... and No

## Slide 70: Are We Getting Any Better?
Some ASes are effectively reducing the number of more specifics that are advertised into the global routing system
Some ASes are increasing the number of more specifics
And some are consistently advertising a significant number of more specifics
There is no net change in the overall distribution and characteristics of more specifics in the routing system.

## Slide 71: Why?
The reasons why we see more specifics in the routing system include:
  Different origination (“hole punching” in an aggregate)
  Traffic engineering of incoming traffic flows across multiple inter-AS paths
  “protection” against route hijacking by advertising more specifics
  Poor routing practices

## Slide 72: Types of More Specifics

## Slide 73: Types of More Specifics
Hole Punching?
Traffic Engineering?
Senseless Routing Vandalism?

## Slide 74: Types of More Specifics
Hole Punching?
Traffic Engineering?
Senseless Routing Vandalism?

## Slide 75: Daily Update Rates
Do more specifics experience a higher update rate than aggregate advertisements?
Lets examine the past 3 years of updates and examine the daily count of prefix updates for root aggregates and more specifics

## Slide 76: Daily BGP Updates

## Slide 77: Relatively Speaking

## Slide 78: More Specifics

## Slide 79: Daily Update Rates
Do more specifics generate a higher update rate than aggregate advertisements?
    Yes – in terms of prefix updates, more specifics are some 4 times noisier than the aggregates in terms of update traffic totals
    More Specifics that “hole punch” (different origin AS) tend to be relatively noisier than other forms of more specifics

## Slide 80: Problem? Not a Problem?
It’s evident that the global BGP routing environment suffers from a certain amount of neglect and inattention

## Slide 81: Problem? Not a Problem?
It’s evident that the global BGP routing environment suffers from a certain amount of neglect and inattention
Could we do better?
  Yes!
  Filtering out more specifics will both reduce table size and also reduce the level of dynamic update in the inter-domain environment

## Slide 82: Problem? Not a Problem?
It’s evident that the global BGP routing environment suffers from a certain amount of neglect and inattention
Should we do better?
  It can be difficult to justify the effort and the cost: the current growth rates of the routing table lie within relatively modest parameters of growth and still sit within the broad parameters of constant unit cost of routing technology
  On the other hand, we need to recognize that we could do a lot better in terms of eliminating routing noise, and achieve this with with a relatively modest amount of effort

## Slide 83
Thank You
Questions?